## Slide 1: Ускорение электронов интенсивными терагерцовыми импульсами
М.Б. Агранат (ОИВТ РАН), А.Н. Степанов (ИПФ РАН)

## Slide 2
План выступления
Мотивация: почему ТГц
Источники мощных ТГц
Формирование начального сгустка электронов
Ускорительные структуры

## Slide 3
Почему ТГц
Ускоряющие поля:
~ 100 МВ/м для 100-200 нс X-band RF ускорител
~ 1 ГВ/м для ~ 1 пс (1 THz)
Характерный допуск на точность изготовления элементов
ускоряющих структур – мкм, лазеры - нм
Порог пробоя ускорительных структур:
Es~ f 1/2 τ -1/4
Нагрев стенок:
Hs ~ τ -1/2

## Slide 4
Накачка: 60 mJ, 10 Hz, cryogenic Yb:YLF,
ТГц: W≈ 65 mkJ, E ~ 1 MV/cm
Наклонный фронт LiNbO3
Wu et al. Optic Express, 18 (2016)
Накачка: 95 fs, 30 mJ, Cr:Mg2SiO4, 1.25 mkm
ТГц: W≈1 mj, E=40 MV/cm
Organic crystal DSTMS
C. Vicario et al. Opt. Letters, 39, 6632 (2014)
Генерация терагерцовых импульсов

## Slide 5
L. Wimmer et al. Nature Physics, 10, p.432 (2014)
Au nanotip 800 nm, 50 fs + THz from light-induced air plasm
Проблема синхронизации электронного пучка и ускоряющего ТГц импульса

## Slide 6
Sha Li et al. Nature Communication (2016)
W tip
ETHZmax = 450 kV/cm
ТГц наклонный фронт
We ~e·k·ETHz·a
k~λ/a
We ~ e·ETHz·λ

## Slide 7
E. Nanni et al. Terahertz-driven linear electron acceleration
Nature Communication (2105)
Ускорение электронов в ускоряющих структурах

## Slide 8
F.X. Kartner et al. Phys. Rev. accelerators and beams
19, 081302 (2016)

## Slide 9
Principles of Acceleration by High-Power Picosecond Pulses
Parameters: period – 300 m, wall thickness - 50 m, aperture width - 3 mm
Proper lengths of channels provide synchronism with particles
THz electric field distribution
S.V. Kuzikov et al. Advanced Accelerator Concepts (2016)

## Slide 10
Copper layers
Aluminum layers
Layer thickness is 50 m
Production technology includes: 1) assembling of copper-aluminum “sandwich”, 2) electroplating of the reflecting cover mirror 2) removal of aluminum in acid.
“Sandwich”

## Slide 11
We_in=50 MeV
We_out≈ 50.4 MeV
For ETHz=10 MV/cm
in a focus of parabola
accelerating gradient
≈ 1.5 MeV/cm

## Slide 12
Short THz pulse field distributions at parabolic mirror focusing for six sequential times
Electric and magnetic field components in parabolic mirror focus
Optimization of focusing parabolic mirror